## Slide 1
Green
Brown
Prepared by Chad Higgins
Image of dual-use sheep pasture field location, late August
Dual-use (agrivoltaic) systems benefit the agricultural industry and the energy industry.
Chad Higgins, Elnaz HassanPour, Steve Good, John Selker, Marc Calaf

## Slide 2
Plant transpiration cools microclimate
Shade % reduces water demands, plant stress
Reduced agricultural water demand leaves more water available.
Cooler PV panels produce more energy
Less stressed plants produce more food, better food
solar excess
A high-functioning dual use system
We can measure all of this!

## Slide 3: more water available for longer under panels
Fig 4: Soil moisture time series (a) 0.2m, (b) 0.4m and (c) 0.6m. For more information: there was 40 mm precipitation over the observation period, i.e. May-Aug 2015.
Orientation, the dashed diagonal is the noon shadow front in August for reference
SFC = solar fully covered (full shade)
SPO = solar partially open (partial shade)
SFO= Solar Fully open (no shade, but in array area)

## Slide 4
90% more biomass
328% more water efficient

## Slide 5
Solar panel efficiency
  decreases with air temp
  increases with wind speed
  decreases with humidity
Modeled with thermodynamics
Field data
Model

## Slide 6: Thermodynamic model applied to globe.

## Slide 7: Energy potential of solar power ranked by land classification: the best place to put solar panels is on croplands

## Slide 8
Solar panels led to an 300%+ increase in the water use efficiency of the cropping system
Solar panels led to a 90% increase in biomass production of the cropping system
Species diversity changed
Solar panels are projected to be more productive when placed over cropping systems

## Slide 9: Conclusions
Plant transpiration cools microclimate
Shade % reduces water demands, plant stress
Reduced agricultural water demand leaves more water available.
Cooler PV panels produce more energy
Less stressed plants produce more food, better food
solar excess
Solar panels led to an 300%+ increase in the water use efficiency of the cropping system
Solar panels led to a 90% increase in biomass production of the cropping system
Solar panels are projected to be more productive when placed over cropping systems

## Slide 10: Caveats and where we are going
Have only investigated pasture conditions
Results likely to change with irrigation
Measurements ongoing or planned to determine
  Nutrient content of forage and soil (in process)
  Genetic sequencing of soil microbiology (in process)
  Sheep health (In process)
  Pollinators (in process)
  Tolatoes (on process)
  Nursery stock (planned this summer)
  Weed, pest and disease impacts (planned, 2020)

## Slide 11
Yes there are some interesting results here in support of dual use, but this isn’t the main takeaway….
If you don’t work with Agriculturalists, you are leaving $ on the table.
The takeaway